Annex C

TECHNICAL SPECIFICATIONS

FOR ITEM 1

SHORT RANGE HAND HELD THERMAL CAMERA

| Ref No. : ____________________ Item No. : ____________________ Item Description : ____________________ |
| --- |
| Manufacturer : ________________________________________________ Origin : ________________________________________________ Model : ________________________________________________ |
| IOM’S SPECIFICATIONS | BIDDER'S SPECIFICATIONS |
| A handheld, infrared thermal imaging camera improving vision in challenging field conditions like dust, smoke and complete darkness. Image resolution: at least 160 x 120 Human activity detection from at least 450 meters away Waterproof and weather proof housing Video-out connector Rechargeable battery capable of operating the device for at least 4 hours without recharging Spare battery On-screen battery level indicator Operating temperature: -20ºC to +50ºC 220V AC adaptor 220V AC Battery charger Training for using of the equipment by qualified personal from the Supplier |  |
| Quantity: 20 pieces |  |
| Delivery site: Ministry of Interior (MoI) |  |
| Delivery period: 30 calendar days |  |
| Warranty: At least 12 months after provisional acceptance supported with document describing the conditions of the warranty. |  |

## _______________________________________

## Supplier’s authorized signature over printed name